## Slide 1
PHARMACEUTICAL DOSAGE FORMS
Tablet Formulation
Process · Excipients · Stability · Challenges
Dosage Form Selected: Compressed Tablet (Immediate Release)
Pharmaceutical Sciences | Formulation & Development

## Slide 2
TABLET: OVERVIEW & TYPES
A tablet is a solid unit dosage form produced by compressing a drug with excipients. It is the most widely used oral dosage form due to accuracy, stability, and ease of manufacture.
Immediate
Release (IR)
Drug released rapidly post-ingestion. Most common.
Extended
Release (ER)
Controlled drug release over hours. Reduces dosing frequency.
Chewable
Tablet
Soft texture, flavored. For pediatrics & antacids.
Dispersible
Tablet
Disintegrates in water before administration.
Focus of this presentation: Immediate Release Compressed Tablet — the reference standard for formulation science.

## Slide 3
TABLET FORMULATION PROCESS
01
API
Characterization
Assess solubility, particle size, polymorphism, hygroscopicity
02
Pre-formulation
Study
Excipient compatibility, drug stability, physicochemical profiling
03
Granulation
Wet / Dry / Direct compression. Improves flow & compressibility
04
Compression
Rotary tablet press. Control hardness, weight, friability
05
Coating
(Optional)
Film coat for protection, taste masking, or aesthetics
06
QC &
Packaging
Dissolution, hardness, disintegration, friability testing
Each step requires rigorous process validation before scale-up to commercial manufacturing.

## Slide 4
EXCIPIENTS USED IN TABLET FORMULATION
Excipients are inactive ingredients that aid manufacturing, stability, and drug release.
Excipient Category | Function | Common Examples | Typical % w/w
Diluent / Filler | Adds bulk to low-dose API | Lactose, MCC (Avicel), Mannitol | 30 – 80%
Binder | Holds granules together | PVP (Kollidon), HPMC, Starch | 2 – 10%
Disintegrant | Promotes tablet breakup in GI tract | Croscarmellose Na, SSG, Starch | 2 – 8%
Lubricant | Prevents sticking to punch/die | Magnesium Stearate, Stearic Acid | 0.25 – 1%
Glidant | Improves powder flow | Colloidal SiO₂ (Aerosil), Talc | 0.1 – 0.5%
Coating Agent | Film coat: protection / appearance | HPMC, Opadry, Eudragit | 2 – 5% weight gain
MCC = Microcrystalline Cellulose · PVP = Polyvinylpyrrolidone · SSG = Sodium Starch Glycolate · HPMC = Hydroxypropyl Methylcellulose

## Slide 5
STABILITY FACTORS
PHYSICAL STABILITY
Moisture / Humidity
Causes softening, sticking, disintegration failure. Control with desiccants.
Temperature
Elevated temp accelerates polymorphic transitions and melting of lubricants.
Light
Photodegradation of light-sensitive APIs (e.g., nifedipine). Use amber packaging.
Mechanical Stress
Poor hardness → friability, capping, lamination during transport.
CHEMICAL STABILITY
Hydrolysis
Water cleaves ester/amide bonds in API. Moisture control is critical.
Oxidation
Free-radical degradation. Use antioxidants (BHA, BHT) or nitrogen purge.
Drug-Excipient Interaction
Maillard reaction: amine APIs + lactose → colored products.
Microbial Degradation
Moisture + organic excipients → microbial growth. Control Aw < 0.6.
ICH Q1A stability guidelines require accelerated (40°C/75% RH) and long-term (25°C/60% RH) testing for all solid dosage forms.

## Slide 6
KEY FORMULATION CHALLENGES
01
Poor Solubility (BCS Class II & IV)
▸ ~40% of new APIs have low aqueous solubility
▸ Solutions: Solid dispersions, nanosizing, cyclodextrins, lipid-based systems
▸ Challenge affects both dissolution rate and bioavailability
02
Poor Flowability & Compressibility
▸ Fine API particles have poor flow → weight variation in tablets
▸ Solutions: Wet granulation, slugging (dry granulation), spray drying
▸ Direct compression preferred but needs good flow excipients
03
Content Uniformity for Low-Dose Drugs
▸ API < 5% of tablet weight is critical — blend uniformity essential
▸ Risk of dose dumping or sub-therapeutic levels
▸ Solutions: Geometric dilution, high-shear mixing, ordered mixing
04
Scale-Up from Lab to Commercial
▸ Process parameters change non-linearly on scale-up
▸ Granule properties, compaction force, coating uniformity all shift
▸ Risk: dissolution profile changes even with same formulation

## Slide 7
QUALITY CONTROL TESTS FOR TABLETS
IN-PROCESS CONTROLS
Test | Acceptance Criterion | Instrument
Hardness | 4–10 kPa (depends on tablet size) | Tablet hardness tester
Thickness | Consistent ±0.1 mm | Micrometer / online sensor
Weight Variation | ±5% of average weight (USP) | Analytical balance
Friability | < 1% weight loss after 100 rotations | Roche friabilator
FINISHED PRODUCT TESTS
Test | Specification | Method
Disintegration | < 15 min (IR tablets) | Disintegration tester
Dissolution | ≥ 80% in 30 min (Q30) | USP Apparatus I or II
Content Uniformity | 85–115% of label claim | HPLC / UV assay
Assay | 98.0–102.0% of declared strength | HPLC
Regulatory Compliance Note
All tablet QC methods must be validated per ICH Q2(R1). Stability studies follow ICH Q1A(R2). Dissolution specifications are set based on bioequivalence data and pharmacopeial requirements (USP/BP/Ph.Eur).

## Slide 8
KEY TAKEAWAYS
Tablet Formulation: Summary
01
Formulation is multi-step —
From API characterization → granulation → compression → coating → QC, each step is interdependent.
02
Excipients are not inert —
They directly impact solubility, stability, release rate, and manufacturability. Selection is science-driven.
03
Stability = ICH compliance —
Physical + chemical stability must be evaluated under real-time and accelerated conditions per ICH Q1A.
04
Challenges are API-specific —
Poor solubility, flow, and content uniformity are the top 3 barriers — each requiring a tailored approach.
05
Scale-up needs validation —
Lab-to-commercial transition is high-risk. Process analytical technology (PAT) helps bridge the gap.